Производитель называется Digital doMaiN

http://www.digital-do-main.com/product/amp.html

All SIT DC amplifier B-1a

Orthodoxy with unique aiming toward the amplifier which coexists

Big power source, the minimum requirement small condenser, shear sea and heat dissipation [rajieta] which are strong in the vibration, A class DC amplifier, the speaker and low the resistance it is necessary OTL etc whose connection is possible to tight aims toward the pure tone, for the high-end amplifier which with the sense of value which is established, the original static induction transistor (SIT) it produces with custom semiconductor process, pulls out the characteristic of SIT and such as the new circuit which is managed includes the unique creation and the monocrystal which adhered to manufacturing method thickly shortest distance wiring by the silver streak, the main amplifier digital restraining, domain which B-1a it delivers to everyone.

Made in Hamamatsu and Japan  It is something which connects 2 B-1a with the amplifier link

Static induction transistor

2SK278B/2SK78B/2SJ78B			2SK77B

Channel 150W+150W 2

Channel 300W 1 (BTL)

Powerful power source

Using the SIT static induction transistor for all signal passes

Using the silver gold wire for signal pass and wiring around the gland

With respect to copper 5mm thick shear sea mechanism, power transformer decrease swing mount

Digital domain B-1a specification

* BackRated output	:	At the time of stereo 150W + 150W (4Ω)

:	At the time of B T L 300W (4Ω)

Input sensitivity	:	At the time of stereo 850mV

:	At the time of B T L 610mV

Input impedance	:	Imbalance 10kΩ

:	Balance 10kΩ

Frequency characteristic	:	DC - 100kHz (+0, −3dB)

Noise distortion factor	:	0.005% or less 10Hz - 1kHz, 10W - 140W (4Ω)

Control operation		:	Input change (balance and imbalance)

:	Output change (stereo and BTL, channel 2 monaural)

:	Channel 2 gearing volume

:	Input trim every of channel

Power source　		:	Voltage AC100V 50Hz/60Hz

:	Electric power consumption 355W (maximum)

External size			:	W218mm×D550mm×H176mm

Weight　　			:	24kg

Desired retail price		:	1,000,000 Yen (classified by tax)

* Concerning the price and specification of the product there are times when it modifies without notice